CUSTOM DESIGN ADA SIGNS

SAMPLE SPEC SHEET

SECTION 10426

SIGNAGE AND GRAPHICS

PART 1    GENERAL

1.01	SECTION INCLUDES

A.	Room signs

1.02	SUBMITTALS

A.	Manufacturers must submit 3 references showing comparable products for projects

completed within the last 5 years.

B.	Manufacturer's Data: Submit manufacturer's descriptive literature and specifications,

including color samples of material for selection, as applicable for approval.

C.	Submit shop drawings listing sign styles, lettering and locations, and overall dimensions

of each sign.

D.	Submit full size sample sign of type, style and color specified including method of

attachment.

1.03	SYSTEM DESCRIPTION

A.	Signage package shall meet the requirements of the Americans with Disabilities Act -

1990 Accessibility Guidelines for Buildings and Facilities and ANSI A117.1 - 1992.

PART 2    PRODUCTS

2.01	MANUFACTURER - [Raised] [Specify Material] Signs

A.	Best Sign Systems, 1202 N. Park Ave., Montrose, CO 8140; Telephone 1-800-235-2378; Fax 1-970-249-0223; E-mail sales@bestsigns.com

B.	Signs shall have the following characteristics:

1.	Tactile characters/symbols shall be raised 1/32 inch from sign plate face [for ADA compliance].

2.	Signs shall be of one-piece construction; added-on and/or engraved characters are

unacceptable.

3.	Text [on signs needing to comply with ADA] shall be accompanied by Grade 2

braille.

4.	All letters, numbers and/or symbols shall contrast with their background - either

light characters on a dark background or dark characters on a light background.

Characters and background shall have matte finish.

BEST SIGN SYSTEMS

MONTROSE, COLORADO 81401

800-235-BEST   FAX 970-249-0223

CUSTOM DESIGN ADA SIGNS

SAMPLE SPEC SHEET - page 2

2.02	SIGNAGE

A.	Sign material shall consist of [insert material], approximately 1/8" [or specify thickness

of material] thick, with background painted a contrasting color. [List any other

characteristics of material].

B.	Lettering style shall be [name of typestyle], upper case [or upper and lower].

C.	Sizes of letters and numbers shall be as follows:

1.	Room numbers shall be 5/8" high [or specify height].

2.	Lettering for room usage and directional identification shall be 5/8" high [or specify height].

3.	Lettering for restroom identification shall be 5/8" high, corresponding symbols shall be 3" high [or specify height].

D.	Letters and numbers shall be centered [or specify location] on sign.

E.	Grade 2  braille [for signs requiring braille] shall be placed directly below last line of

letters or numbers [or specify location].

F.	Specify corner style.

2.03	SIGN SIZE

A.	Per Schedule

2.04	SIGN SCHEDULE

- Provide the following interior signs: [Provide complete list of required signs including text and symbols, if any. Indicate sizes and quantity of each.]

BEST SIGN SYSTEMS

MONTROSE, COLORADO 81401

800-235-BEST   FAX 970-249-0223

CUSTOM DESIGN ADA SIGNS

SAMPLE SPEC SHEET - page 3

PART 3   EXECUTION

3.01	EXAMINATION

A.	Examine installation areas to insure that proper condition exist for timely completion of

installation.

3.02	PREPARATION

A.	Verify that mounting locations and height for each sign will comply with ADA

Accessibility Guidelines.

B.	Mounting locations should be smooth and free of all dirt, dust, grease, etc.

3.03   INSTALLATION

A.	Mount signs level and plumb using manufacturer's recommended standard mounting

hardware of vinyl foam tape or holes and screws.

B.	Remove excess adhesives, etc. from exposed sign surfaces as recommended by adhesive

manufacturer.  Clean sign surfaces as needed.

BEST SIGN SYSTEMS

MONTROSE, COLORADO 81401-0577

800-235-BEST   FAX 970-249-0223